FAST IDLE ADJUSTING SCREW

Testing

1.   Disconnect the #18 hose from the fast idle unloader.

#18 VACUUM HOSE

FAST IDLE UNLOADER

CAP

2.   Open and close the throttle fully to engage the fast idle cam.

3.   Start the engine.

Fast idle should be 3.200 ± 500 min 1 (rpm)

Adjust the fast idle speed, if necessary, by turning the fast idle adjusting screw.

5.	Reconnect the hose.

6.	Warm up to normal operating temperature (the cooling fan comes on).

When the engine warms up, it speed should drop below 1,400 min-1 (rpm) as the unloader pulls the internal choke linkage off the fast idle cam.

VACUUM PUMP/GAUGE

• If fast idle does not drop below 1,400 min-1 (rpm), disconnect the #18 hose, and check the vacuum.

#18 VACUUM HOSE

•	If there is no vacuum, check the #18 vacuum line for proper connection, cracks, blockage or disconnected hose. If OK, replace the thermovalve.

•	If there is vacuum, replace the fast idle unloader, and then inspect the choke coil tension and linkage (page 11-122).

11-127