Carburetor

г- Automatic Choke and Fast Idle [2-Carbureted Engine]

Description

This system provides easy engine starting under a wide range of air temperatures. The system consists of the following:

a)	The choke valve and its linkage system

b)	The choke opener (page 11-130).

c)	The fast idle system (page 11-133).

The choke valves are located in the air intakes of the carburetors. When the engine is not running, the choke valve angle is determined by the thermowax valve. When the engine is running, the choke opener also affects the choke valve angle.

The choke opener adjusts the choke valve for increased air flow once the engine begins to fire. It operates in two steps according to coolant temperature.

The automatic choke system is controlled by the thermowax valve; as coolant temperature rises, the valve's piston extends which causes the fast idle cam to gradually rotate and decrease idle speed.

Engine coolant is fed through a passage in the carburetor's cast front bracket to prevent carburetor icing and to improve cold driveability by improving vaporization of the air/fuel mixture. Since excessive heat can cause fuel percolation, a thermovalve is used to shut off the coolant flow at temperatures above the thermovalve set temperature.

COOLANT

COOLANT

TO

THERMOVALVE

TO	Ж"^

INTAKE MANIFOLD

ROD

CHOKE OPENER

11-128