Carburetor

- Choke Opener [2-Carbureted Engine]

Description

Thermovalve operates to open the choke valve in response to engine coolant temperature. When the engine coolant temperature is below the set temperature of thermovalve (1 5°C), it opens and manifold vacuum is bled from the opener. In this situation the choke opener diaphragm is retracted to an intermediate position because of the balance between the vacuum and the spring force of the choke opener.

When the engine coolant temperature exceeds the set temperature of thermovalve (1 5°C), it closes to shut off the vacuum bleed and allows the choke opener to retract fully and pull the choke valve open.

THERMOVALVE

I   г

11-130